Exploiting IA-32 redundancy
Charles Paulet

---
Instructions encoding (IA-32e)

---
Operands encoding
Operand encoding = addressing method + operand type
Abbreviations revealing possible mutations :
Abbr	Description
E	A ModR/M byte follows the opcode and specifies the operand.
G	The ModR/M reg part selects a general register
I	Immediate data
b	Byte
v	Word, doubleword or quadword depending on operand-size attribute

---
Opcodes encoding
- 1, 2 or 3-byte opcodes
- 3 opcode tables
- ModR/M and SIB bytes for specific addressing modes

---
Example (ADD Gv, Ev)

---
Register operands and the ModR/M byte
Instruction	bytes	opcode	ModR/M
add eax, ebx	01 d8	01	d8 (mod: 0b11) (reg: 0b011) (rm: 0b000)
add ebx, eax	03 d8	03	d8 (mod: 0b11) (reg: 0b011) (rm: 0b000)
add eax, ebx	03 c3	03	c3 (mod: 0b11) (reg: 0b000) (rm: 0b011)

---
Register operands and the SIB byte
When SIB.scale is 0b00 :
Instruction	bytes	SIB
mov rax, qword ptr [rbx + rcx]	48 8b 04 0b	0x0b (index: 0b001, rcx) (base: 0b011, rbx)
mov rax, qword ptr [rcx + rbx]	49 8b 04 19	0x19 (index: 0b011, rbx) (base: 0b001, rcx)
Instruction	bytes	SIB
mov byte ptr [eax + ebx], 5	67 c6 04 18 05	0x18 (index: 0b011, ebx) (base: 0b000, eax)
mov byte ptr [ebx + eax], 5	67 c6 04 03 05	0x03 (index: 0b000, eax) (base: 0b011, ebx)

---
Duplicate opcode extensions
Group 0xf6
Instruction	bytes	ModR/M reg
test bl, 0x10	f6 c3 10	0b000
test bl, 0x10	f6 cb 10	0b001
Group 0xf7
Instruction	bytes	ModR/M reg
test ebx, 0xaabbccdd	f7 c3 dd cc bb aa	0b000
test ebx, 0xaabbccdd	f7 cb dd cc bb aa	0b001

---
Duplicate opcodes in 32-bit mode
Group 1 have duplicated opcodes for 0x80 and 0x82 on x86 when working with imm8 (or Ib)
Instruction	bytes
add byte ptr [eax], 0x10	80 00 10
add byte ptr [eax], 0x10	82 00 10
Also works for ADD, OR, ADC, SBB, AND, SUB, XOR, CMP depending on the ModR/M reg

---
Duplicate opcodes in 32/64-bit mode
Group 1 have duplicated opcodes for 0x81 and 0x83 when working with imm8 (or Ib)
Instruction	bytes
add eax, 0x10	83 c0 10
add eax, 0x10	81 c0 10 00 00 00
add rax, 0x10	48 83 c0 10
add rax, 0x10	48 81 c0 10 00 00 00

---
Duplicates for the acc register
The acc register can be mutated using the x4 and x5 opcodes
Instruction	bytes
add al, 0x10	04 10
add al, 0x10	80 c0 10
add eax, 0x10	05 10 00 00 00
add eax, 0x10	81 c0 10 00 00 00
add eax, 0x10	83 c0 10
add eax, 0x10	48 05 10 00 00 00 00
add rax, 0x10	48 81 c0 10 00 00 00
add rax, 0x10	48 83 c0 10
And for ADD, OR, ADC, SBB, AND, SUB, XOR, CMP, depending on the ModR/M reg

---
Duplicates using zero displacements
Instruction	bytes	ModR/M mod
add dword ptr [eax], eax	67 01 00	0b00
add dword ptr [eax + 00], eax	67 01 40 00	0b01
add dword ptr [eax + 00000000], eax	67 01 80 00 00 00 00	0b10

---
SIB scale/index corner case
When SIB.index is 0b100, SIB.scale is useless
Instruction	bytes	SIB.scale
mov byte ptr [0xaabbccdd], 0xff	c6 04 25 dd cc bb aa ff	0b00
mov byte ptr [0xaabbccdd], 0xff	c6 04 65 dd cc bb aa ff	0b01
mov byte ptr [0xaabbccdd], 0xff	c6 04 a5 dd cc bb aa ff	0b10
mov byte ptr [0xaabbccdd], 0xff	c6 04 e5 dd cc bb aa ff	0b11
Instruction	bytes	SIB.scale
mov byte ptr [ebp + 0x56], 0xff	c6 44 25 56 ff	0b00
mov byte ptr [ebp + 0x56], 0xff	c6 44 65 56 ff	0b01
mov byte ptr [ebp + 0x56], 0xff	c6 44 a5 56 ff	0b10
mov byte ptr [ebp + 0x56], 0xff	c6 44 e5 56 ff	0b11

---
Legacy prefixes
In 32-bit mode, we can omit some legacy prefixes:
Instruction	bytes
add qword ptr [eax], eax	67 01 00
add qword ptr [eax], eax	01 00
Some instructions might accept one or more prefixes:
Instruction	bytes
nop	90
nop	66 90
nop	66 67 90
nop	66 66 67 90

---
Logic transformations
Like zeroing registers
Instruction	bytes	ModR/M
xor bx, bx	66 31 db	0xdb (mod: 0b11) (reg: 0b011) (rm: 0b011)
xor ebx, ebx	31 db	0xdb (mod: 0b11) (reg: 0b011) (rm: 0b011)
sub bx, bx	66 29 db	0xdb (mod: 0b11) (reg: 0b011) (rm: 0b011)
sub ebx, ebx	29 db	0xdb (mod: 0b11) (reg: 0b011) (rm: 0b011)
mov ebx, 0	bb 00 00 00 00	0x00 (mod: 0b00) (reg: 0b000) (rm: 0b000)
mov rbx, 0	48 c7 c3 00 00 00 00	0xc3 (mod: 0b11) (reg: 0b000) (rm: 0b011)

---
Going further
- Signatures/pattern-matching bypasses?
- Cmake / C&C module?
- Steganography?
- LLVM passes?
- post-compilation / LIEF frontend?

---
Tool 1: transasm
implementing the techniques discussed
based on capstone
there are still mutations waiting to be
found and implemented into transasm
we can use it as a mutation engine and
add more constraints

---
Tool 2: asmshell
ASM REPL based on capstone, keystone, unicorn

---
Key takeaways
- It’s easy to get started with capstone, keystone, unicorn
- x86 encoding knowledge can be reused elsewhere (minimal disassembler)